## Slide 1
b8008
Resurrecting the World’s First 8-Bit Microprocessor
A cycle-exact Intel 8008 in VHDL, built with an AI pair programmer
Robert Rico
Notes: One-liner intro. "In 1972 Intel shipped the first 8-bit microprocessor. I spent 8 months bringing it back — and tonight it’s running on the table." Deck color story: Intel blue until we reach the FPGA; charcoal+yellow (Lattice) from there — the theme itself says whose world we’re in. Never say it out loud. Chip photo: Konstantin Lanzet, Wikimedia Commons, CC BY-SA 3.0.

## Slide 2
ACT I — WHAT
The Intel 8008 (April 1972)
• World’s first 8-bit microprocessor
• 3,500 transistors, 10 µm PMOS
• 18 pins — for a CPU
• 500 kHz clock; instructions take 5, 8, or 11 T-states
• 16 KB address space (14-bit)
• Seven 8-bit registers (A, B, C, D, E, H, L)
• 48 instructions
Notes: Emphasize 18 pins — that single number causes most of the weirdness coming up. Modern context: an ATtiny has more pins. Chip photo: Konstantin Lanzet, Wikimedia Commons, CC BY-SA 3.0.

## Slide 3
ACT I — WHAT
Built for a terminal, rejected by its buyer
• 1969-70: CTC (Computer Terminal Corp., later Datapoint) designs the Datapoint 2200 "programmable terminal" — CPU built from ~100 TTL chips
• CTC asks Intel and Texas Instruments to shrink it to one chip
• TI’s TMX 1795 (1971): technically first 8-bit CPU chip — never shipped
• Intel’s chip: late, and slower than CTC’s TTL board — CTC walks away
• Intel keeps the rights in trade, sells it as the 8008
Notes: The ISA was CTC’s design, not Intel’s. TI beat everyone to silicon but never productized — the 8008 outlasted it by shipping.

## Slide 4
ACT I — WHAT
Your laptop still carries its DNA
8008
1972
8080
1974
8086
1978
x86
today
The instruction-set lineage in every PC today traces back to a terminal company in San Antonio, Texas.
And in 1974, the SCELBI-8H — arguably the first personal computer — was built around this chip. That’s where our demo software comes from.
Notes: Bridge slide — plants SCELBI now so the demos later have context.

## Slide 5
ACT I — THE QUIRKS
Weirdness #1 — Two clocks, never high together
The 8008 needs two non-overlapping clock phases (φ1, φ2).
No single clock pin. External circuitry must generate both phases with guaranteed dead time between them.
Get the overlap wrong → internal buses fight → undefined behavior.
Real capture: the FPGA generating φ1/φ2 on my bench
Notes: These scope shots are from my bench — this is the FPGA generating the two phases. In 1972 you built this from discrete logic before the CPU would even blink.

## Slide 6
ACT I — THE QUIRKS
Weirdness #2 — One bus, three jobs
18 pins means 8 data pins total. So the bus is time-multiplexed, three ways, every machine cycle:
T-state | What’s on the 8 pins
T1 | Address, low byte
T2 | Address high 6 bits + cycle type
T3 | The actual data
External latches must grab each piece at the right instant.
Fig. 1, 8008 User’s Manual — one instruction cycle
Notes: "Tri-plexed" bus. Every memory access is a little three-act play. The CPU also broadcasts its internal state on pins S0-S2 so external logic can follow along.

## Slide 7
ACT I — THE QUIRKS
Weirdness #3 — It boots by being interrupted
• No reset vector. At power-on the PC is garbage.
• The *only* way to start it: assert the interrupt line and jam an instruction onto the bus (typically RST 0)
• Startup is an interrupt. Interrupts are instruction injection. It’s injection all the way down.
• Intel’s own reference design (SIM8-01) needed dozens of TTL support chips just to make the CPU usable.
SIM8-01: find the CPU. (Hint: the small box in the middle.)
Notes: This is why "just wire up the CPU" was never an option — in 1972 or now. The support glue is half the project.

## Slide 8
ACT I — THE QUIRKS
Weirdness #4 — There is no program counter
…there are eight of them.
The PC is whichever slot of an 8 × 14-bit address stack the stack pointer selects.
• CALL = SP moves forward (old slot keeps the return address)
• RET = SP moves back
• 7 levels of nesting; the 8th CALL silently wraps onto the oldest
No stack in memory. No PUSH/POP of data. 1972 had opinions.
slot 7
slot 6
slot 5 ← SP (this IS the PC)
slot 4
slot 3
slot 2
slot 1
slot 0
8 × 14-bit address stack
Notes: Remember this one — it becomes the heart of the final design later. Implemented structurally, exactly as drawn, the stack-wrap behavior falls out for free.

## Slide 9
ACT II — FPGA PRIMER
The FPGA I chose: Lattice ECP5-5G Versa
• LFE5UM5G-45F — 44K LUTs, 1.9 Mb block RAM, 5 Gbps SerDes
• Dev board: DIP switches + LEDs become the 8008’s front panel; UART over USB is the terminal
• Best-in-class open-source toolchain support: Yosys + nextpnr know this chip inside out
• Design runs at 25 MHz system clock; timing closes at ~95 MHz. The 8008 needs 500 kHz.
The entire 1972 computer system: 1,672 LUTs — 3% of the chip
Notes: THEME FLIP: we just left Intel’s world (blue) and entered Lattice’s (charcoal + yellow) — the deck stays this way to the end. Numbers from the real b8008_basic build reports: 1,672/43,848 LUT4s (3%), 8/108 block RAMs (7%), fmax ~95 MHz vs 25 MHz system clock. The chip is comically oversized for the job — the whole 1972 rack fits in a corner of it.

## Slide 10
ACT II — FPGA PRIMER
30-second FPGA primer
• A chip full of uncommitted logic blocks and programmable wiring
• You describe a circuit; the toolchain configures the chip to *become* it
• Not emulation, not software — it is the circuit, in real silicon, in parallel
• This project targets a Lattice ECP5-5G using a fully open-source toolchain (GHDL + Yosys + nextpnr)
Notes: For the software folks: the 8008 design isn’t simulated on the board — the board is wired up as an 8008. All that 1972 support glue — clocks, latches, ROM, RAM, UART — fits inside the same chip.

## Slide 11
ACT II — FPGA PRIMER
Hardware description languages in one slide
Two mainstream ways to describe digital hardware — same job: describe registers and logic; tools synthesize real gates.
Verilog — C-flavored, terse, dominant in US industry
always @(posedge clk)
if (en)
count <= count + 1;
VHDL — Ada-flavored, verbose, strongly typed
process(clk) begin
if rising_edge(clk) then
if en = '1' then
count <= count + 1;
end if;
end if;
end process;
This project: VHDL, one file per functional block.
Notes: Don’t linger. "Verbose but strict — it catches a class of mistakes at compile time, which matters when your collaborator is an AI."

## Slide 12
ACT III — THE AI-AIDED PROJECT
The project: 8 months, 3 attempts
Nov 2025 → Jul 2026 — 297 commits. 3 iterations, 2 complete bottom-to-top rewrites.
✗ s8008
monolithic, single-cycle
Worked in simulation.
Broke on hardware.
✗ v8008
multi-cycle rewrite
Collapsed under its own
complexity.
✓ b8008
block-based, cycle-exact
SILICON VALIDATED
Built in collaboration with Claude (Anthropic’s AI) — every line reviewed, tested, and frequently rejected
Notes: Set expectations honestly: this was NOT "AI, build me an 8008." Eight months of iteration, and I threw the whole thing away twice. Here’s what the first two attempts taught me.

## Slide 13
ACT III — THE AI-AIDED PROJECT
s8008: when "all tests pass" lies to you
The monolithic version passed its whole simulation suite.
On the FPGA, ALU operations returned garbage.
• Single-cycle timing masked bugs simulation couldn’t see
• One 1,500-line file nobody — human or AI — could fully reason about
Rule adopted: nothing is "done" until it’s proven on silicon.
Notes: This failure defined the whole methodology afterward: sim-pass is a hypothesis, hardware is the proof. The v8008 rewrite then failed differently — too clever, too entangled. Two failures, one diagnosis: complexity nobody could reason about.

## Slide 14
ACT III — THE AI-AIDED PROJECT
The AI wrote most of the VHDL. Here’s why that worked.
It worked because I could tell when it was wrong.
• I had to learn the 8008 cold: T-states, machine cycles, every ISA quirk
• Built isa.json — every opcode mapped to its documented T-state sequence — as ground truth
• Wrote a Python "oracle" emulator to cross-check behavior before touching hardware
• 28-test regression suite; cycle counts diffed against the datasheet automatically
The AI multiplied effort. The verification was the job.
// docs/isa.json - ground truth
{
"operation": "CAL",
"D[7:0]": "01XXX110",
"num_states_execution": 11,
"num_cycles": 3,
"cycle_1": {
"T1": "PCL OUT",
"T2": "PCH OUT",
"T3": "FETCH INSTR.",
...
"cycle_3": {
...
"T4": "REG.a TO PCH",
"T5": "REG.b TO PCL" }}
Notes: The transferable lesson for this audience: AI collaboration shifts your work from writing to specifying and verifying. You must know enough to catch it being confidently wrong — and it will be. SEGUE: "So attempt #3 needed a design that a human AND an AI could each fully reason about. Turns out Intel drew it for us in 1972."

## Slide 15
ACT IV — THE DESIGN THE FAILURES FORCED
The fix: build Intel’s own block diagram. Literally.
Attempt #3:
One module per block.
No cleverness.
Fig. 3, 8008 User’s Manual (1973)
Notes: After two failures from complexity, the answer was radical simplicity: stop inventing an architecture and copy the one on the datasheet. Walk the diagram: address stack, scratchpad registers, ALU, instruction register/decoder, timing & control. Every box becomes a VHDL file.

## Slide 16
ACT IV — THE DESIGN THE FAILURES FORCED
Design rule: every module is dumb
29 VHDL files. Each block:
• Does one job, ~50–100 lines
• Knows nothing about instructions, interrupts, or other modules
• Responds only to explicit control signals
• Has its own testbench
All the intelligence lives in one place: the timing & control unit.
Timing & Control Unit
(the only smart module)
address
stack
stack
pointer
register
file
ALU
instr.
decoder
control signals only — no module knows what a "JMP" is
Mirrors Fig. 3 box-for-box —
the diagram IS the architecture
Notes: Direct answer to the s8008 postmortem: when a module can’t know about instructions, it can’t harbor an instruction-specific bug. Debugging becomes: which control signal was wrong, and when? Also the AI payoff: a 70-line module with one job is something Claude gets right — and something I can fully review.

## Slide 17
ACT IV — THE DESIGN THE FAILURES FORCED
The whole stack pointer. All of it.
if reset = '1' then
sp <= (others => '0');
elsif rising_edge(clk) then
if phi1_rising = '1' then
if stack_push = '1' then
sp <= sp + 1; -- wraps 7 -> 0
elsif stack_pop = '1' then
sp <= sp - 1; -- wraps 0 -> 7
end if;
end if;
end if;
src/b8008/stack_pointer.vhdl
69 lines including comments.
It has never had a bug.
It doesn’t know what CALL is. It doesn’t know interrupts exist.
It counts.
Notes: CALL/RET/RST semantics — even the stack-wrap behavior from Weirdness #4 — emerge from structure, not from logic.

## Slide 18
ACT V — HOW DO I KNOW IT WORKS?
The real test suite was written in 1974
Directed tests prove what you thought to test.
Period software proves the machine.
• SCELBI floating-point calculator (1974)
• HEXPAWN — self-modifying learning game (1973)
• STARS (Byte magazine, 1976)
• Pi digit generator, Mandelbrot renderer
• SCELBAL BASIC (1976)
Each ported with a minimal, documented change ledger — I/O shims and memory-map constants only.
Notes: If a self-modifying 1973 game and a floating-point interpreter both run, the CPU is right in ways no directed test can claim. This software exercised corners I’d never have thought to test.

## Slide 19
ACT V — HOW DO I KNOW IT WORKS?
Verification scorecard
Check | Result
Regression suite | 28/28
Cycle-exact T-states vs datasheet (all 27 timing classes) | 27/27
Interrupt suite | 10/10
Hardware ISA self-test, running on the board | 46/46
Flags spec-exact (INR/DCR preserve carry; rotates carry-only) | ✓
Interrupts at instruction boundaries only (User’s Manual Fig. 2) | ✓
Notes: "Cycle-exact" means: not just the right answer — the right answer in exactly the number of clock states the 1972 datasheet specifies, for every instruction class. Optional: swap table for green run_all_tests.sh terminal screenshot.

## Slide 20
ACT VI — LIVE PROOF
Live: 1970s software on the board
LIVE
1. Pi — 50 digits via Machin’s formula, multiprecision arithmetic (2013 program for SCELBI hardware)
2. SCELBI Calculator (1974) — 23-bit floating point: 12.2 X 2.2 = 26.84
3. HEXPAWN (1973) — self-modifying code: it learns as it loses
4. Finale — the tiny OS: power on → BASIC → MON → monitor dumps the tokenized program from RAM → G 1FB6 → back in BASIC, program intact
Notes: Rig (rig slide cut — say it here): Versa board, minicom 115200 8N1, local echo off, DEL for rubout; monitor commands D/W/L/G; DIP switches = interrupts + READY/WAIT.
DEMO CHEAT SHEET (verify commands before talk):
• Pi: L in monitor → send hex via send_hex.py → G 0040. ~75 s at 500 kHz for 50 digits — narrate history while it grinds. 49/50 digits correct; the 50th is the ORIGINAL program’s guard-byte truncation — great trivia beat.
• Calc: load, G, type 12.2 X 2.2 = live.
• HEXPAWN: play 2 quick games, point out it stops making the losing move. DROP CANDIDATE if running long.
• Tiny OS: power-cycle board into b8008_basic bitstream. Type a 3-line FOR/NEXT program, RUN, MON, D the program region, G 1FB6, LIST — program survived.
• Fallback: pre-recorded terminal captures of all four in case hardware misbehaves.

## Slide 21
ACT VI — TAKEAWAYS
What I’d tell you to steal
• Dumb modules, smart control — structure beats cleverness; the block diagram was right all along
• Simulation passing is a hypothesis. Hardware is the proof.
• AI pair programming works when you own the ground truth — I specified and verified; it multiplied
• Old software is the best test suite — it encodes assumptions no one thinks to write down
• 1972 engineers did all of this with 3,500 transistors. Respect.
Notes: Close on the human point: the 8008’s designers had no simulator, no regression suite, no second chances on a mask set.

## Slide 22
Questions?
Robert Rico
Project: github.com/robertrico/intel-8008-vhdl
SCELBAL: Jim Loos (jim11662418/8008-SBC)
Period software: Mike Willegal’s SCELBI archive (willegal.net)
Original SCELBAL: Arnold & Wadsworth, 1976
Notes: Fill in real repo URL if/when public. Invite people to type at the machine — most memorable 8-bit demo is the one they drive.